## Slide 1: A unique processor architecture meeting LLVM IR and the IoT
Dávid Juhász david.juhasz@imsystech.com

## Slide 2: Compiling with LLVM
LLVM
High-Level Programming Language
LLVM Assembly / IR
Your Typical Target ISA
LLVM Front-end
LLVM Back-end
LLVM Middle-end
Notes: Start with LLVM 101: formats and steps when compiling with LLVM

## Slide 3: Improving Efficiency by Lifting Target
LLVM
High-Level Programming Language
LLVM Assembly / IR
Your Typical Target ISA
LLVM Front-end
LLVM Back-end
LLVM Middle-end
Imsys ISA for LLVM
Big gap Complex translation
Reducing the gap
Notes: What this talk is about
  ISAs are usually designed with no respect for compiler IR
  We create an ISA tailor-made for LLVM
  We expect improved efficiency in several aspects, detailed later…

## Slide 4: Agenda
Imsys Company and the IoT
Imsys Lean Processing Technology
Imsys ISA for LLVM

## Slide 5: Imsys AB
Device
Module
IC
IP
Notes: Swedish semiconductor SME
Products
  Devices
  Modules
  IC
  IP

## Slide 6: Networked Embedded Controllers
Notes: History as supplier of networked embedded controllers
  Proven core technology
Retargeting for the IoT
  Good match for our values

## Slide 7: Imsys EMBLA Single Controller Solution for the IoT
Notes: Imsys EMBLA
  Single controller board
  with graphics
  Various IO capabilities via extension board

## Slide 8: High-Level Software Platform
Application Code
C/C++
Java
Executable Binary
LLVM
Integrated Development Environment
Notes: Software platform overview
  Eclipse-based IDE for connecting to the development board
  Application Code can be
    Java
    C/C++ compiled with LLVM

## Slide 9: Improving Efficiency by Reducing the ISA Gap
LLVM
High-Level Programming Language
LLVM Assembly / IR
Your Typical Target ISA
LLVM Front-end
LLVM Back-end
LLVM Middle-end
Imsys ISA for LLVM
Big gap Complex translation
Reducing the gap
Notes: Now let’s look under the hood to see what is the basis of the Imsys lean processing technology: what makes the Imsys processor different from the mainstream and how that allows us to dedicate an ISA for LLVM Assembly.

## Slide 10: Abstraction Layers
Imsys Processor Core
Imsys Instruction Set Support
ISAL
ISAJ
Application Code
JAVA
Assembly/C/C++
Notes: Check out the main levels of abstractions – the traditional way
  Processor core and its supported instruction sets
  Software code in high-level – System software and application
    Java with dedicated ISAJ for native execution
    Assembly/C/C++ targeting ISAL

## Slide 11: A Forgotten Layer of Abstraction
Software
Hardware
Microcode
Hardware
Software
Notes: Today’s typical categorization: Hardware & Software
There could be an extra layer in between, which gives Imsys processors unique abilities: microcode

## Slide 12: The Processor Architect’s Best Friend
IO
Microprogram
Mult.
ALU
MEM
Ctrl.
Addr.
Operation-Oriented Hardware Architecture
Microinstruction
Notes: Microcode enables architects to master their hardware softly
  Microprogram consisting of microinstructions in memory
  Hardware core executes microinstructions
  A microinstruction consists of fields
  Each fields controls functional units of the processor core directly
    Including sequence control, which selects the next microinstruction to execute
The microcode runs an Operation-Oriented Architecture focusing on the task at hand

## Slide 13
Microcode, what is it good for?
Complete Deterministic Control
Flexibility
Soft-Reconfigurability
Minimal Hardware
Maximum Efficiency
Notes: List the main characteristics provided by microcoding
  Complete deterministic control – direct control over all functional parts of the core
  Minimal hardware – control by microcode, hence no deep pipeline, no out-of-order or speculative execution, no cache hierarchy, no complex state
  Maximum efficiency – no wasted computation, maximum utilization of hardware
  Flexibility – implement any computation with high efficiency, making the processor multi-purpose
  Soft-reconfigurability – microcode in memory may be changed at any time on demand

## Slide 14: Abstraction Layers Revisited
Imsys Processor Core
Imsys Instruction Set Support
Application Code
Software
Microcode
Hardware
ISAL
Notes: Match abstraction levels to our case
  Processor Core is hardware
  Instruction Set Support is in microcode
  Application Code is software
  Note that Instruction Sets are the lowest level software interface to use the microcoded features, they belong to software
  A compiler, LLVM, matches the high-level application code to the instruction set

## Slide 15: A Unique Balance between Hardware and Software
Instruction Set Architecture
Application
Compiler
Microcode
Balanced Rich ISA
Domain-specific Operations
Instruction Set Architecture
Operation-Oriented Hardware Architecture
Notes: Application code is made executable by a compiler targeting an ISA
  ISA is typically defined by hardware
Consider an operation-oriented hardware architecture with microcoding
A microcode-defined ISA is lifted from the hardware
A unique balance between software and hardware supports all parties to improve efficiency
  Systems architects design in complex domain-specific operations and deliver a compiler-friendly ISA with optimized hardware utilization
  Compiler designers target a machine supporting a balanced rich ISA with high-level operations

## Slide 16: Improving Efficiency by Matching LLVM Assembly
LLVM
High-Level Programming Language
LLVM Assembly / IR
Your Typical Target ISA
LLVM Front-end
LLVM Back-end
LLVM Middle-end
Imsys ISA for LLVM
Big gap Complex translation
Reducing the gap
Notes: We have just looked into the basics of the Imsys Lean Processing Technology, now turn towards our tailor-made instruction set for LLVM.

## Slide 17: Matching LLVM Assembly
LLVM Assembly
ISAL
Semantically matching instructions
LLVM back-end for ISAL
Simple, efficient, general LLVM
LLVM middle-end
Direct use of optimizations
Notes: How does ISAL match LLVM Assembly?
  ISAL matches LLVM Assembly by having semantically matching instructions
    Complexity propagated into ISAL implementation
How does the semantic match help?
  LLVM back-end for ISAL
    Simple and efficient back-end relying mostly on general LLVM facilities
    No complex translation as no semantical difference
  LLVM middle-end applies general optimizations to LLVM Assembly
    Directly exploiting platform-independent LLVM optimizations due to the semantical match
    Moreover, general LLVM optimizations are enough, no need for much architecture-specific magic

## Slide 18: Meeting a Constrained Reality
 | LLVM Assembly | ISAL
Operations | Instructions & intrinsic functions | Additional system operations
Single Value Types | Virtually unlimited | Set of integer, floating point, pointer, and vector types
Registers | Unlimited | Register windows
Arguments | Source and destination registers | Registers with support of accumulating in source registers, immediate values
Binary Representation | Bitcode | Custom dense binary coding
Notes: !Hidden original of the next animated slide!
LLVM Assembly is a theoretical model with characteristics that render it impossible to implement directly
  Need to add special operations for bookkeeping
    Moving data to/from/between registers
    Managing execution
    Handling I/O
  Need to select single value types to support
  Need to define actual register set
  Better to support special kinds of arguments to optimize register usage
  Better to optimize binary representation to improve code density, execution time, and power consumption

## Slide 19: Meeting a Constrained Reality
LLVM Assembly
ISAL
Operations
Instructions &
intrinsic
functions
Single Value Types
Virtually unlimited
Set of integer, floating point,
pointer, and vector types
Registers
Unlimited
Register windows
Arguments
Source and
destination registers
Registers with support of
accumulating in source registers,
immediate values
Binary Representation
Bitcode
Custom dense binary coding
Additional
system operations
Notes: LLVM Assembly is a theoretical model with characteristics that render it impossible to implement directly
  Need to add special operations for bookkeeping
    Moving data between and immediate values into registers
    Managing execution state
    Handling I/O
  Need to select single value types to support
  Need to define actual register set
  Better to support special kinds of arguments to optimize register usage
  Better to optimize binary representation to improve code density, execution time, and power consumption

## Slide 20: Optimized Operation Sequences
a ≔ a + b
opcode
dst
src1
src2
Accumulating in source register
opcode
src1
src2
Immediate values
a ≔ a + 42
move b 42
add a a b
add.imm a a 42
add.upd.imm a 42
add a a b
add.upd a b
Notes: Regular instructions with destination and source registers are bloating binary code, so we have special variants.
Accumulating in source register – happens quite often
  Consider example: a = a + b
  The corresponding regular operation needs 3 arguments
  A special accumulating (in-place update) variant works only with 2 arguments
  Binary size is reduced
Working with immediate values
  Consider example: a = a + 42
  Using the corresponding regular instruction needs the immediate value to be moved into a register by an extra instruction
  A special form with one immediate argument can do the same work as one instruction with 3 arguments
  Even better, combine the two: accumulating variant with one immediate argument does it as one instruction with 2 arguments
  Binary size is reduced again
ISAL has different variants operations to improve code density

## Slide 21: Optimized Binary Representation
Chart: Number of Instructions
| Intstruction Lengths (Bytes)
1 | 7
2 | 198
3 | 465
4 | 258
5 | 161
6 | 11
7 | 0
8 | 0
9 | 1
10 | 4
Variable-length Instructions
Maximize Code Density
Optimize Microcode Size
Minimize Execution Time
Notes: Efficiently encoding such a rich set of instructions requires variable-length instructions
  Instruction lengths between 1 and 10
  Average 3.4
Binary format is defined considering the following goals
  Software perspective makes us maximize code density
    Frequent operations have shorter instruction
  The microcode implementation should be economic with optimized size
    Common instruction formats share decode logic
    Grouped instructions share operation logic
  Performance counts, so we need to minimize execution time
    Time for decoding is dependent on binary representation
      Simple operation should have short instruction
    Time for performing operation may be dependent on binary representation
      It could overlap with argument decoding if similar operations are grouped together

## Slide 22: Average Binary Size of TI Suite
Chart: 
Imsys | 1
Cortex-M0+ | 1.36
Cortex-M4 | 1.46
x86 | 1.8
x64 | 2.2
ARM Cortex requires 35%+ more, Intel 80%+ more program memory.
Notes: Preliminary ISAL code density figures as average binary size of TI Suite benchmarks normalized to ISAL.

## Slide 23
Dávid Juhász david.juhasz@imsystech.com
ISAL
Imsys Processor Core
Imsys Firmware
Imsys Lean Processing Technology
LLVM Assembly
LLVM back-end for ISAL
Imsys ISA for LLVM
Imsys EMBLA with ISAL
Leaner is Meaner
Notes: Concluding with the main points
  Imsys Lean Processing Technology
    Operation-Oriented Hardware Architecture
    Microcode-defined ISA
  Imsys ISA for LLVM
    How ISAL matches LLVM Assembly
    Some design considerations
ISAL and its software ecosystem are currently under development, and planned to be released for Imsys EMBLA in next year