## Slide 1
HPVM: Performance, Portability, Programmability and Approximation for Heterogeneous Parallel Systems
Vikram Adve
With:
Maria Kotsifakou, Hashim Sharif, ♣ Prakalp Srivastava, Adel Ejjeh, Akash Kothari, Benjamin Schreiber, Yifan Zhou
Sarita Adve and Sasa Misailovic
University of Illinois at Urbana-Champaign
♣Google Brain
Supported by: NSF, DARPA, SRC, ONR, Intel, Amazon

## Slide 2: Heterogeneous SoCs are Ubiquitous
Heterogenous parallelism and specialization are critical for energy efficiency, performance

## Slide 3: IBM EPOCHS Project: Autonomous Car SoC
DSSoC’s Full-Stack Integration
HPVM for
Programmability

## Slide 4: Example: A Modern Mobile SOC
Main Memory
Interconnect
Modem
GPS
DSP
DSP
GPU
A/V Hardware Accelerators
DSP
Multi-media
CPU
L1 Cache
L2 Cache
CPU
L1 Cache
Vector
Vector
different parallelism models
Incompatible memory systems
different hardware ISAs
And different SoCs have different combinations of such hardware!
Key to Programmability and Portability:
Common abstractions for heterogeneous parallel hardware

## Slide 5: Interface Levels and Key Benefit
CPUs + Vector SIMD Units
…
GPU
DSP
Domain-specific Accelerators
FPGA
"Hardware" ISA
Virtual ISA
Language-neutral Compiler IR
Language-level Compiler IR
General-purpose prog. language
Domain-specific prog. language
GPU ISAs, SIMD ISAs, TPU,
Domain-specific accelerators, …
IBM’s MIR , PTX, HSAIL,
HPVM, SPIR
Delite IR, HPVM, MLIR, OSCAR
Delite DSL IR, XLA, TVM, …
CUDA, OpenCL, OpenAcc,
OpenMP, Python, Julia
TensorFlow, MXNet, Halide, …
Hardware innovation
Object-code portability
Compiler investment
Language innovation
App. performance
App. productivity

## Slide 6: At What Level Should We Abstract Away Heterogeneous Parallelism?
CPUs + Vector SIMD Units
…
GPU
DSP
Domain-specific Accelerators
FPGA
Hardware ISA
Virtual ISA
Language-neutral Compiler IR
Language-level Compiler IR
General-purpose prog. language
Domain-specific prog. language
Too diverse
to define a
uniform interface
Also too diverse …
Much more
uniform
GPU ISAs, SIMD ISAs, TPU,
Domain-specific accelerators, …
IBM’s MIR, PTX,
HSAIL, SPIR, HPVM
Delite IR, HPVM, MLIR, OSCAR
Delite DSL IR, XLA IR, TVM, …
CUDA, OpenCL, OpenAcc,
OpenMP, Python, Julia, …
TensorFlow, MXNet, Halide, …

## Slide 7: Existing Solutions for Heterogeneous Systems
General-purpose parallel languages lack high-level abstractions
  Designed for parallel computing experts
  OpenMP 4.5, OpenACC, …
“SIMT” prog. languages are GPU-friendly but expressivity is limited
  CUDA, OpenCL
DSLs attractive but still too technical for domain specialists
  TensorFlow, MXNet, Halide, …
Virtual ISAs enable portability and performance
  But current ones have expressivity problems of CUDA, OpenCL
  PTX, HSAIL, SPIR

## Slide 8: LLVM Derivatives for Parallel Systems
System | Focus
LLVM | Short SIMD: SSE, AVX, Neon …
Polly | Polyhedral transforms, scheduling
Tapir | Homogeneous SMPs
OpenMP, OpenCL, CUDA | GPUs
LegUp | FPGAs
TensorFlow XLA | TPU, GPU
MLIR | Tensors, polyhedral transforms
None attempt to capture diverse heterogeneous parallelism

## Slide 9
The HPVM Program Representation
A common parallel abstraction
Compiler IR + Virtual ISA + Run-time scheduling
hpvm.cs.Illinois.edu

## Slide 10: Heterogeneous Parallel Virtual Machine
Goal: Programmability for Heterogeneous Parallel Systems
Use HPVM for:
Portable object code
Retargetable parallel compiler IR and system
Run-time scheduling
Translators
HPVM
Virtual ISA
Runtime Scheduler
C+HPVM
Keras
TensorFlow
Other
DSLs
Front ends
CPUs + Vector SIMD Units
…
GPU
DSP
Domain-specific Accelerators
FPGA
Halide
Kotsifakou et al., PPOPP 2018

## Slide 11: Abstraction of Parallel Computation
Dataflow Graph with side effects
Vector
VA = load <L4 x float>* A
VB = load <L4 x float>* B
…
VC = fmul <L4 x float> VA, VB
Hierarchical
or
Graph nodes – coarse-grain or fine-grain computational tasks
Graph edges – explicit data transfer between nodes
Loads and stores – implicit communication via shared memory
Hierarchical – multiple levels of nested parallelism

## Slide 12: HPVM Node Parallelism
Static Dataflow Graph
Dynamic Dataflow Graph (conceptual)
[N]
1
2
N
Node instantiation
Similar to instances of a CUDA or OpenCL kernel body
HPVM supports 1-3 dimensional grids: 1D, 2D, 3D, …
Notes: A graph node represents a static computation, and any such node can be “instantiated” in a rectangular grid of dynamic node instances, representing independent parallel instances of the computation (in which case, the incident edges are instantiated as well, as described later).
The hierarchical dataflow graphs naturally capture all the important kinds of coarse- and fine-grain data and task parallelism in heterogeneous systems. In particular, the graph structure captures coarse-grain task parallelism (including pipelined parallelism in streaming computations); the graph hierarchy captures multiple levels and granularities of nested parallelism; the node instantiation mechanism captures either coarse- or fine-grain SPMD-style data parallelism; and explicit vector instructions within leaf nodes capture fine- grain vector parallelism (this can also be generated by automatic vectorization across independent node instances).
We also believe it maps well to FPGA and semi-custom hardware accelerators. We currently have two projects in the pipeline – one where we are using HPVM for code generation on FPGAs and another where we are compiling HPVM to a very novel mixed signal accelerator for ML
Essentially the hierarchical DFG abstraction of HPVM allows us to capture N different parallelism models through a single unified parallelism model

## Slide 13: E.g., Edge Detection in Images
Pipelined (task) parallelism with streaming input images
Medium-grain data parallelism within pipeline stages
Fine-grain data parallelism in most stages

## Slide 14: Extension of LLVM Virtual Instruction Set
  Express new instructions as LLVM intrinsic functions
Intrinsics for Constructing Graphs | 
i8* llvm.hpvm.createNode1D(i8* F, i32 n) | Create node with n dynamic instances executing node function F (similarly, llvm.hpvm.createNode2D/3D)
i8* llvm.hpvm.createEdge(i8* Src, i8* Dst, i1 ReplType, i32 sp, i32 dp, i1 isStream) | Create edge from output sp of node Src to input dp of node Dst.
void llvm.hpvm.bind.input(i8* N, i32 ip, i32 ic, i1 isStream) | Bind input ip of current node to input ic of child node N; similarly llvm.hpvm.bind.output
Intrinsics for Quering Graphs | 
i8* llvm.hpvm.getNode() | Return a handle to the current dataflow node
i8* llvm.hpvm.getParentNode(i8* N) | Return a handle to the parent of node N
i32 llvm.hpvm.getNumDims(i8* N) | Return the number of dimensions where N is replicated.
i64 llvm.hpvm.getNodeInstanceID.[xyz](i8* N) | Get index of current dynamic instance of node N in dimension x, y, or z
i64 llvm.hpvm.getNumNodeInstances.[xyz](i8* N) | Get number of dynamic instances of node N in dimension x, y, or z
Intrinsics for Memory Allocation and Synchronization | 
i8* llvm.hpvm.malloc(i64 nBytes) | Allocate a clock of memory of size nBytes and return pointer to it
i32 llvm.hpvm.atomic.xchg(i8* m, i32 v), i32 llvm.hpvm.atomic.add(i8* m, i32 v) … | Atomic swap, atomic fetch-and-add, etc on shared memory locations
void llvm.hpvm.barrier() | Local synchronization barrier across dynamic instances of current leaf node

## Slide 15: Extension of LLVM Virtual Instruction Set
  Express new instructions as LLVM intrinsic functions
Intrinsics for Constructing Graphs | 
i8* llvm.hpvm.createNode1D(i8* F, i32 n) | Create node with n dynamic instances executing node function F (similarly, llvm.hpvm.createNode2D/3D)
i8* llvm.hpvm.createEdge(i8* Src, i8* Dst, i1 ReplType, i32 sp, i32 dp, i1 isStream) | Create edge from output sp of node Src to input dp of node Dst.
void llvm.hpvm.bind.input(i8* N, i32 ip, i32 ic, i1 isStream) | Bind input ip of current node to input ic of child node N; similarly llvm.hpvm.bind.output
Intrinsics for Quering Graphs | 
i8* llvm.hpvm.getNode() | Return a handle to the current dataflow node
i8* llvm.hpvm.getParentNode(i8* N) | Return a handle to the parent of node N
i32 llvm.hpvm.getNumDims(i8* N) | Return the number of dimensions where N is replicated.
i64 llvm.hpvm.getNodeInstanceID.[xyz](i8* N) | Get index of current dynamic instance of node N in dimension x, y, or z
i64 llvm.hpvm.getNumNodeInstances.[xyz](i8* N) | Get number of dynamic instances of node N in dimension x, y, or z
Intrinsics for Memory Allocation and Synchronization | 
i8* llvm.hpvm.malloc(i64 nBytes) | Allocate a clock of memory of size nBytes and return pointer to it
i32 llvm.hpvm.atomic.xchg(i8* m, i32 v), i32 llvm.hpvm.atomic.add(i8* m, i32 v) … | Atomic swap, atomic fetch-and-add, etc on shared memory locations
void llvm.hpvm.barrier() | Local synchronization barrier across dynamic instances of current leaf node
Intrinsics for Interacting with the Host | 
i8* llvm.hpvm.launch(i8* F, i8* args, i1 isStream) | Launch graph with function F asynchronously.
void llvm.hpvm.wait(i8* GraphID) | Wait for completion of graph GraphID
void llvm.hpvm.push(i8* GraphID, i8* args) | Push args as streaming input of graph GraphID
i8* llvm.hpvm.pop(i8* GraphID) | Read next streaming output of graph GraphID

## Slide 16: Optimization and Code Generation
Intel Xeon E5 core i7
CPU
nVidia GeForce
GTX 680 GPU
Intel
AVX
Front
end
Source
program
.ll (with HPVM intrinsics)
Developer site
User site
HPVM-to-
NVPTX
HPVM-to-
LLVM
HPVM-to-
SPIR
HPVM graph optimizer
Code-gen: Bottom-up on graph hierarchy
Key:
any node
any device
reuse vendor
back ends
LLVM
X86-64
code-gen
Intel
AVX
code-gen
LLVM
PTX
code-gen
Altera
FPGAs
HPVM-to-
OpenCL
Altera
AOC
HLS tool
buildDFG module pass

## Slide 17: Code Generation Strategy – HPVM to NVIDIA PTX
  Graph structure determines
    kernel function
    meaning of HPVM query intrinsics
Kernel Code
Host Code
Leaf node function f
HPVM query intrinsics to
OpenCL function calls
Link with libclc
NVPTX backend
PTX kernel
NVVM
  Calls to OpenCL runtime
    kernel setup and call
  Encapsulate in node genFunc
  Expose to x86 backend
Leverage NVPTX back-end

## Slide 18: Code Generation Strategy – HPVM to OpenCL
  Graph structure determines
    kernel function
    meaning of HPVM query intrinsics
Kernel Code
Host Code
Leaf node function f
HPVM query intrinsics to
OpenCL function calls
OpenCL backend
OpenCL kernel
LLVM with OpenCL calls
  Calls to OpenCL runtime
    kernel setup and call
  Encapsulate in node genFunc
  Expose to x86 backend
Leverage OpenCL back-end
Notes: Alternative version. For alternative path, targeting OpenCL backend

## Slide 19: HPVM-C Front End
clang
main.{c,cc}
hpvm.h
main.ll
opt -GenHPVM
main.ll
main.hpvm.ll
HPVM-C source program,
containing HPVM function calls.
Declarations of HPVM
C/C++ functions
Module Pass that converts the
HPVM-C function calls to HPVM intrinsics.
Text representation of HPVM.
  Source to LLVM
  LLVM to HPVM

## Slide 20: HPVM Compilation Steps
opt -BuildDFG
[-LocalMem
-DFG2LLVM_NVPTX]
-DFG2LLVM_X86
-ClearDFG
main.host.ll
  Code Generation: HPVM to LLVM
main.hpvm.ll
main.kernels.ll
Module Pass that deletes the internal HPVM
representation from memory and the node
functions from the host module.
Module Pass that generates either all, or
the remainder of the host module.
If GPU target is selected. Generates GPU kernel
for nodes executing on GPU and CPU host code
to launch the kernels in the host module.
Module Pass that converts the text representation
to the internal HPVM graph representation.
Generated Host Module
Generated Kernel Module
Notes: (LocalMem is an analysis pass - returns information about the allocation nodes to the DFG2LLVM_NVPTX pass.)

## Slide 21: HPVM Compilation: Final Linking
  Host Pre-link
hpvm-rt.bc
HPVM runtime
main.host.ll
llvm-link
files.ll
Generated with clang
main.host.linked.ll
Linked Host Module
  Final Code Generation (e.g., GPU)
main.host.linked.ll
clang (X86 backend)
main.kernels.ll
main.kernels.cl
llvm-cbe
main.host.linked

## Slide 22: Flexible Node-to-Device Mapping
N graph nodes
K devices
Static or dynamic
mappings
Static: Single HPVM program permits KN mappings
Dynamic: Modify mappings at run-time per node launch

## Slide 23: Evaluation: Goals and Methodology
Multicore: Intel Xeon E5 core i7
Vector ISA: AVX
GPU: nVidia GeForce GTX 680 GPU; 1536 cores; 2GB
Comparisons with separate hand-tuned codes
  OpenCL (Parboil): SPMV, sgemm, stencil, lbm, bfs, tpacf, cutcp
  Hand-tuned for GPU: opencl_nvidia (5), opencl_base (2)
  Hand-tuned for AVX: Same version as GPU except stencil, bfs

## Slide 24: HPVM vs. Hand-tuned for GPU
Within 22% of hand-tuned
Normalized Execution Time (left: HPVM; right: OpenCL baseline=1.0)
Lower is better

## Slide 25: HPVM vs. Hand-tuned for Intel AVX
Within 20% of hand-tuned except lbm
Normalized Execution Time (left: HPVM; right: OpenCL baseline)
Lower is better

## Slide 26: Evaluation: Goals and Methodology
Multicore: Intel Xeon E5 core i7
Vector ISA: AVX
GPU: nVidia GeForce GTX 680 GPU; 1536 cores; 2GB
Comparisons with separate hand-tuned codes
Flexible static scheduling
  Edge detection in grayscale images
  Map 6 pipeline stages to 3 PEs: Scalar, GPU, Vector
  36 = 729 possible mappings from one program

## Slide 27: Example: Static Scheduling of Graph Nodes
Chart: 
| SSSSSS | VVVVVV | GGGGGG | VVVVSV | GGGGSG | VVSVVS | GGSGGS
Frame Rate (frames/s) | 0.36766 | 9.3733 | 101.2712 | 8.7863 | 49.2752 | 1.526 | 1.5378
Frames / sec
Map 6 pipeline stages to 3 hardware units: Scalar, GPU, Vector
36 = 729 pipeline configurations from a single HPVM code
Bars show 7 of 729 configurations. Higher is better.
…
1
3
2
4
5
6

## Slide 28: Evaluation: Goals and Methodology
Multicore: Intel Xeon E5 core i7
Vector ISA: AVX
GPU: nVidia GeForce GTX 680 GPU; 1536 cores; 2GB
Comparisons with separate hand-tuned codes
Flexible static scheduling
Flexible dynamic scheduling

## Slide 29: Example: Dynamic Scheduling of Instances
Scheduling granularity:
  Per (offloaded) node per data item
Data available to runtime policies:
  Node ID
  Data item number
  Any system monitor information available
Three example scheduling policies:
  Static Node Assignment Policy
  Static Data Item Assignment Policy
  Dynamic, on GPU when available (emulated)

## Slide 30: Dynamic Scheduling of Instances
Video stream of 1280 x 1280 grayscale frames
(By emulation) GPU availability alternates ON / OFF
ON
OFF

## Slide 31: Dynamic Scheduling of Instances
Instantaneous frame rate for grayscale edge detection
Flexible offline and online scheduling across hardware
Single performance-portable code representation
Expressive: several kinds of parallelism
ON
OFF

## Slide 32: Evaluation: Summary
HPVM performance comparable to hand-tuned codes
Flexible static scheduling: PN static mappings for HPVM program of N nodes
Flexible dynamic scheduling: Can reassign DFG nodes flexibly under changing load
Vector ISA: Intel Xeon E5 core i7 + AVX
GPU: nVidia GeForce GTX 680 GPU; 1536 cores; 2GB
Benchmarks: Parboil: SPMV, sgemm, stencil, lbm, bfs, tpacf, cutcp
Baseline: Separately hand-tuned OpenCL versions
Notes: Evaluation on PPOPP paper, i.e. NVPTX and SPIR, dynamic scheduling.

## Slide 33: Open Source Release: HPVM v0.5
HPVM IR + verify pass
LLVM-9 patches: v. small
Lowering: HPVM-C to DFG
Back-ends:
  NVIDIA GPU via OpenCL
  Intel / AMD host
Future: Intel AVX, Altera FPGAs
HPVM IR spec.
HPVM-C spec.
Installation guide
  https://gitlab.engr.illinois.edu/llvm/hpvm-release
Test cases:
  Regression tests
  Unit tests
  Parboil
  Edge-detect image pipeline
  CAVA camera pipeline

## Slide 34: Main Updates for Release
Port to LLVM 9.0
New LLVM-to-OpenCL back end using revived C back-end (from Julia project)
Better testing framework
Intel AVX
nVidia GeForce
GTX 680 GPU
Intel Xeon E5 core i7
CPU
HPVM-to-
OpenCL
HPVM-to-
SPIR
HPVM-to-
LLVM
HPVM graph optimizer
Code-gen: Bottom-up on graph hierarchy
Intel
AVX
code-gen
LLVM
X86-64
code-gen
NVIDIA
PTX
code-gen

## Slide 35: Ongoing and Future Work
Ongoing 1: HPVM-to-FPGA code generation
Goal: Hardware-agnostic programming of FPGAs
Ongoing 2: Approximate computing support
Goal: Make accuracy-aware optimizations easier to use
Future 1: New DSL front-ends
Goal: Interoperable DSLs for complete edge applications
Future 2: MLIR integration
Goal: New back-ends for MLIR; polyhedral opts for HPVM

## Slide 36: Possible Step: HPVM in MLIR
Multi-level IR: Framework for multiple interoperable IRs
Emphasis: Dense array, tensor operations
What is MLIR?
Dialects: namespaces with associated ops
Examples: “affine”, “llvm”, “linalg”, “gpu”, etc.
MLIR dialects
HPVM would benefit from polyhedral opts,
HPVM may get new front-ends (very few today)
MLIR may get more back-ends, e.g., FPGA, NPU
MLIR would get accuracy-aware optimizations
HPVM dialect:
goals

## Slide 37: Summary
HPVM: portability + performance for heterogeneous systems
  virtual ISA
  compiler IR
  runtime representation
Questions?

## Slide 38: ApproxHPVM IR: Intrinsics & Quality Metrics
L1 Error:
L2 Error:
ApproxHPVM IR Portable
Quality metrics:
ApproxHPVM IR Tensor Intrinsics:

## Slide 39: Keras Compiler Workflow