## Slide 1: Optimization of SDR Applications on Heterogeneous Systems-on-Chip (SoCs)
Samet E. Arda1, Anish Krishnakumar2, A. Alper Goksoy2,
Nirmal Kumbhare3, Joshua Mack3, Anderson L. Sartor4,
Ali Akoglu3, Radu Marculescu5, and Umit Y. Ogras2
  1Arizona State University
  2The University of Wisconsin–Madison
  3The University of Arizona
  4Carnegie Mellon University
  5The University of Texas at Austin

## Slide 2: Motivation
Domain-Specific Systems-on-Chip (DSSoC):
  General-purpose,
  Special-purpose, and
  Hardware accelerator cores
Acc-3
Acc-1
Acc-2
ARM
big
CPU
ARM
big
CPU
ARM
big
CPU
ARM
big
CPU
ARM LITTLE CPU
ARM LITTLE CPU
ARM LITTLE CPU
ARM LITTLE CPU
Acc-3
Acc-1
Acc-1
Acc-1
Acc-2
DSSoC
Better performance
Higher energy-efficiency

## Slide 3: Approach
Full-System Simulation
System-Level Simulation
Hardware Emulation
Slow
Low-level details
Hard to analyze
No scalability
Significant developmental effort
No flexibility
Limited scalability
Faster
Very fast
High degree of modularity
Facilitates algorithmic
development
Controlled level of abstraction
Highly scalable

## Slide 4: Proposed Solution: DS3 Framework
Resource Database
Resource types
Task Latencies
Resource state
Simulation Kernel
Implements schedule
Updates simulation state
Scheduler & DTPM
Plug & play selection
Heuristic schedulers
Tabular schedulers
Report
Power, Performance,
Energy, Schedule
Job / Task Generator
Stochastic job arrival
Domain applications
DS3
Scheduler Algorithms
DTPM
Algorithms
Analytical Models
(Power, Thermal, Interconnect)
Hardware Profiling
Design Space Exploration
Evaluation of scheduling algorithms
Resource management algorithm studies

## Slide 5: Built-in Schedulers: Heuristics
Consider a set of PEs and a task graph with tasks
  : Estimated Execution Time
  : Estimated Availability Time
  Data Availability Time
  : Estimated Completion Time
Minimum Execution Time (MET) Scheduler
Earliest Task First (ETF) Scheduler

## Slide 6: Built-in Schedulers: Constraint Programming
Constraint programming (CP) utilizes concepts of IBM ILOG CPOptimizer [1]
An interval variable x is a decision variable represent
  an activity, operation or a task
Constraints on an interval variable x:
  span(x,{x1, ...,xn}) states if x is present, it starts together with first present interval in {x1, ...,xn} and ends together with last one
  alternative(x,{x1, ...,xn}) models an exclusive alternative between {x1, ...,xn}: if interval is present then exactly one of intervals {x1, ...,xn} is present and x starts and ends together with chosen one.
  no_overlap({x1, ...,xn}) states permutation{x1, ...,xn} defines a chain of non-overlapping intervals
  end_before_start(xi,xj,delay) constrains at least given delay to elapse between end of xi and start of xj.
[1] Laborie, P. IBM ILOG CP Optimizer for detailed scheduling illustrated on three problems. Int. Conf. on AI and OR Techniques in Constraint Programming for Combinatorial Optimization Problems. 2009, pp. 148–162.

## Slide 7: Built-in Schedulers: Constraint Programming
Constraints of model:
Objective function:
Let be a set of DAGs under consideration for scheduling. Then, an interval variable defines DAG in system where
Let denote set of tasks in a DAG . Then, is an interval variable for a task where
Let represent number of PE in a system. Then, is an optional interval variable for task if it can be executed on PE where and

## Slide 8: A Simple Scheduling Case Study
Schedule for a simple DAG with 3 different schedulers
Application DAG
Topcuoglu, H., Hariri, S. and Wu, M.Y., 2002. Performance-effective and low-complexity task scheduling for heterogeneous computing. IEEE transactions on parallel and distributed systems, 13(3), pp.260-274.
Task Profile
Execution time profile of tasks in the DAG on 3 different processing elements
Schedulers
MET ETF CP
Task | P0 | P1 | P2
0 | 14 | 16 | 9
1 | 13 | 19 | 18
2 | 11 | 13 | 19
3 | 13 | 8 | 17
4 | 12 | 13 | 10
5 | 13 | 16 | 9
6 | 7 | 15 | 11
7 | 5 | 11 | 14
8 | 18 | 12 | 29
9 | 21 | 7 | 16

## Slide 9: SDR Applications – Block Diagrams
Wireless communication and radar systems
(a)
(b)
Wireless Communications
WiFi-A Transmitter & Receiver
Low-power single-carrier TX & RX
Radar Applications
Pulse Doppler
Radar Correlator

## Slide 10: SDR Applications – DAG Representations
Wireless communication and radar systems
WiFi-A Transmitter
WiFi-A Receiver
Pulse Doppler
Radar Correlator

## Slide 11: A Detailed Scheduling Case Study
Multiple streaming SDR applications executed simultaneously
Stochastic injection of applications based on various distributions
SoC Configuration
Type of Processing Element | Number of Cores
Arm LITTLE architecture | 4
Arm big architecture | 4
Matrix multiplication hardware accelerator | 2
FFT hardware accelerator | 4
Viterbi decoder hardware accelerator | 2
Scheduler Comparisons
Compare scheduler performance for simultaneous
streaming applications in DSSoCs

## Slide 12: DTPM Case Study
Multiple streaming domain-specific applications executed simultaneously
Evaluate power and energy-based metrics
Obtain a pareto-energy frontier with different DTPM policies
Operating Points
Type of Processing Element | Frequency
Arm LITTLE architecture | 0.6 GHz – 1.4 GHz
Arm big architecture | 0.6 GHz – 2.0 GHz
DTPM Policy Comparisons
Compare energy and energy-delay product (EDP)
for simultaneous streaming applications in DSSoCs

## Slide 13: Design Space Exploration
Identify number and types of PEs using early design space exploration
Workload-based data driven approach and a guided search
SoC Configurations
Type of PE |  |  | Area (mm2) | Average Job Execution (μs) | Energy per Job (μJ/job)
ID | FFT | Viterbi |  |  | 
1 | 0 | 1 | 14.94 | 2606 | 1744
2 | 0 | 1 | 14.94 | 1824 | 1244
3 | 2 | 1 | 15.82 | 293 | 589
4 | 4 | 0 | 16.29 | 1212 | 957
5 | 4 | 1 | 16.56 | 274 | 584
6 | 6 | 3 | 19.29 | 264 | 582
Design Space Exploration Results
Identify pareto-frontier using metrics such as energy, area and performance to choose the processing elements in a DSSoC

## Slide 14: Example Video Demonstration
* Video accelerated for the purpose of demonstration

## Slide 15: Closing Remarks
A Python-based system-level simulation framework for DSSoCs to:
  Compare scheduling algorithms
  Evaluate dynamic power-thermal management (DTPM) techniques
  Conduct extensive design space exploration studies
DS3 calibrated to Odroid-XU3 and Zynq ZCU-102 with an average error of 5%
Envision DS3 to pave the way for easy and rapid exploration of DSSoCs
DS3: A open-source tool that supports easy and rapid exploration of domain-specific systems-on-chip (DSSoCs)
https://github.com/segemena/DS3

## Slide 16: Acknowledgement
This article is based on research sponsored by Air Force Research Laboratory (AFRL) and Defense Advanced Research Projects Agency (DARPA) under agreement number FA8650-18-2-7860. The U.S. Government is authorized to reproduce and distribute reprints for Governmental purposes notwithstanding any copyright notation thereon. The views and conclusion contained herein are those of the authors and should not be interpreted as necessarily representing the official policies or endorsements, either expressed or implied, of Air Force Research Laboratory(AFRL) and Defense Advanced Research Projects Agency (DARPA) or the U.S. Government.