## Slide 1: Hardening Linux Kernel Subsystems by Architectural Capabilities
Zahra Tarkhani
@ztfasr
ztarkhani@microsoft.com
This Photo by Unknown author is licensed under CC BY.

## Slide 2: Outline
Introduction
Background
Morello Linux state
Capability-based hardening
Opportunities & security considerations
Summary

## Slide 3: Linux Security Subsystems
Proper OS hardening is hard and complex
  Various SW-based CFI and fuzzing techniques
  Still seeing many vulnerabilities
Various security features
  DAC, MAC, LSMs, eBPF, seccomp, etc
  Corse-grained privilege separation
Recent HW-security features
  TEE/enclave, PAC, MTE, MPU, SMMU, TZASC/TZPC, RDC, XPPU, SPM
  Different designs and protection capabilities
  Several features on the same SoC

## Slide 4: CHERI
Capability-based security concepts are old
Very long history in the University of Cambridge
  A hardware/software/semantics co-design project
  Fine-grained memory protection leading to increased memory safety.
  Scalable compartmentalization.
Extends ISAs with new capability-aware instructions.
  MIPS, RISC-V, ARMV8.A

## Slide 5: Morello-CHERI
Extends the Armv8.2-A (aarch64 only)
It implements 129-bit CHERI capabilities, simplified as capabilities in this supplement, with compressed bounds
Validity Tag: Providing integrity protection.
Permissions: Limiting operations that can be performed.
Bounds: Limiting how the value can be used, for example, for memory access.
An object type: Supporting higher-level software encapsulation (e.g., Unsealing operations).
Controlled non-monotonicity (via exceptions, executive/restrictive, unsealing ops)

## Slide 6: Morello-CHERI
The behaviour of SVC, HVC, and SMC are not affected by System permission.​

## Slide 7: Morello-CHERI
Capability-extended registers
  e.g., Program Counter Capability (PCC)
  CVTD: Convert pointer to capability
  SCBNDS (register): Set Bounds (register).
  ...
  PE (executive and restrictive modes)

## Slide 8: Morello-CHERI
Capability-extended exceptions

## Slide 9: Resources
Many resources are available:
  https://www.cl.cam.ac.uk/research/security/ctsrd/cheri/
  https://www.arm.com/architecture/cpu/morello
  https://git.morello-project.org/
  Board request: https://www.dsbd.tech/get-involved/morello-board-request/
  Arm® Architecture Reference Manual Supplement Morello for A-profile Architecture

## Slide 10: Morello-Linux
Morello-Linux ABI
  A pure-capability ABI (CONFIG_CHERI_PURECAP_UABI)
  Many kernel features are added
  All pointers passed to or provided by the kernel via syscalls are capabilities
    e.g., mmap returns capability.
    Pointers in structs and unions pointed to by syscall arguments, recursively
      (e.g., iov->iov_base for readv()).
    More proper syscall hardening is needed.
  Address space management changes to handle capabilities
  https://git.morello-project.org/morello/kernel/linux/-/wikis/Morello-pure-capability-kernel-user-Linux-ABI-specification

## Slide 11: Morello-Linux
Relatively easy dev environment (FVP and dev board)
  e.g., debian and busybox
  After few steps & repo init & sync
    ./build-scripts/build-all.sh -p <fvp/soc> -f debian
  https://git.morello-project.org/morello/docs/-/blob/morello/mainline/user-guide.rst

## Slide 12: Morello-Linux
Minimal changes when enabling kernel security features
  CONFIG_BPF_JIT=y,CONFIG_TRUSTED_KEYS=y, CONFIG_TEE=y, CONFIG_OPTEE=y, CONFIG_IMA=y CONFIG_SECURITYFS=y, CONFIG_ENCRYPTED_KEYS=y,CONFIG_TCG_TPM=y …etc
  An example of minor issues when enabling kernel TEE support:

## Slide 13: Morello-Linux
cheri-aware uaccess:
  About 47 places to change (e.g., sched/core, syscall.c, selinux/hooks.c, ipc/msg.c, fs, etc)
ret = put_user(send_len, (__cheri_tocap int * __capability) (int __user *) p);

## Slide 14: Morello-Linux
cheri-aware uaccess:
  About 47 places to change
  e.g., sched/core, syscall.c, selinux/hooks.c, ipc/msg.c, fs, etc
There are helper funcs to speed up the process:
  __cheri_tocap and __cheri_fromcap
  So many more helpers

## Slide 15: Improving CHERI-aware privilege separation
Currently mainstream supports one kernel root capability

## Slide 16: Improving CHERI-aware privilege separation
Combining SW-defined permissions with HW-defined permissions
  CHERI_PERM_SYSCALL
    authorising system calls from $pcc
    syscall sandboxing
  CHERI_PERM_SW_VMEM
    restrict the ability to change the page mapping underlying a capability
  Better combinations for Linux sandboxing mechanisms?
  Improving CHERI-aware privilege separation
Principled approaches and compartmentalization abstractions
  e.g., subprocesses, co-procs, intra-kernel trust domains

## Slide 17: Opportunities and security considerations
Clear and HW-protected security boundaries within the kernel
  LSMs, eBPF, seccomp, namespaces, etc

## Slide 18: Opportunities and security considerations
More secure C/C++ systems stack and extensible compartmentalization
  OS, hypervisor, secure kernels/TEE, etc

## Slide 19: Opportunities and security considerations
More secure C/C++ systems stack and extensible compartmentalization
  OS, hypervisor, secure kernels/TEE, etc
  Integration with Linux security subsystems
    For both hardening the features and HW-assisted guarantees for users
  Integration with other HW-security features
  Compartmentalization tools
  More secure debuggers and traces?
  ...